#JOB DESCRIPTION                                         ##
#############################################################

# bilayer equilibration


#############################################################
## ADJUSTABLE PARAMETERS                                   ##
#############################################################

structure    mem.psf
coordinates  mem.pdb
#binvelocities min_mem.vel

set start_temperature   0
set hold_temperature    $temp
set outputname min_mem.md

firsttimestep      0


#############################################################
## SIMULATION PARAMETERS                                   
# Input
paraTypeCharmm      on
parameters          par.prm
temperature         0


# Force-Field Parameters
exclude             scaled1-4
1-4scaling          1.0
cutoff              12.0
switching           on
switchdist          10.0 #Cutoff-2
pairlistdist        14.0  #Cutoff+2
stepspercycle       10
margin 2.5


# Integrator Parameters
timestep            2.0  ;# 2fs/step
rigidBonds          all  ;# needed for 2fs steps
nonbondedFreq       1
fullElectFrequency  2
useSettle           on   ;#If rigid bonds are enabled #use
#non-interactive SETTLE alg to keep waters rigid


# Constant Temperature Control
#langevin            off    ;# do langevin dynamics
#langevinDamping     5     ;# damping coefficient (gamma) of 5/ps
#langevinHydrogen    no    ;# don't couple langevin bath to hydrogens
#langevinTemp        $temp ;#langevin temperature is
#defined in protocol section

#Affects the output. Wrapping does not affect the simulation.
wrapWater           on
wrapAll             on


#Pressure Control
useGroupPressure yes ;# needed for rigidBonds
useFlexibleCell no
useConstantArea no

langevinPiston        on
langevinPistonTarget  1.01325 ;#  in bar -> 1 atm
langevinPistonPeriod  100.
langevinPistonDecay   50.
langevinPistonTemp    $temp

# Periodic Boundary Conditions
cellBasisVector1 79.72   0   0
cellBasisVector2 0   81.60   0
cellBasisVector3 0    0   98.1
cellOrigin 0.0   0.0   0.0

#PME (for full-system periodic electrostatics)
PME                 yes
PMEGridSpacing      1.0 ;#Using good default. Let NAMD set the grid.

PMEGridSizeX        80
PMEGridSizeY        90
PMEGridSizeZ        100

# Output
binaryoutput       off
outputName         $output

restartfreq 2500
dcdfreq 2500
xstFreq 2500
outputEnergies 2500
outputPressure 2500


#############################################################
## EXTRA PARAMETERS                                        ##
#############################################################

constraints off

#############################################################


#############################################################
## EXECUTION SCRIPT                                        ##
#############################################################

# Minimization # ( 10 ps )
minimize            5000

#RELAXATION PROTOCOL
 350000 steps
# 14 frames (dcdfreq=2500)
# 700 ps     (timestep=2fs)

 Heat +1K in 0.4ps
for { set TEMP 0 } { $TEMP < $temp } {
incr TEMP 1 } {
       langevinTemp $TEMP
       reinitvels $temp
       run 200
}

#Adjust environment to final conditions
langevin            on    ;# do langevin dynamics
langevinDamping     5     ;# damping coefficient (gamma) #of 5/ps
langevinTemp $temp
reinitvels $temp

#Constraints release protocol


#Free dynamics for 50 ps
constraintScaling 0
run 25000